## Slide 1
Making Sorting 3× Faster
with SIMD Vector Units & Multi-Core Parallelism
PDC Final Project · SIMD Bitonic Sort · AVX2 + OpenMP
3.0×
Peak Speedup
12
CPU Threads
2M
Elements Sorted
35/35
Tests Passed
Intel Core i7-12th Gen · 6 cores / 12 threads · AVX2 · GCC 15 · Windows 11

## Slide 2
Base Library — simd_bitonic
Open-source SIMD bitonic sort · AVX2 path · Batcher odd-even merge network
What the library does
· Sorts floating-point arrays using 256-bit AVX2 registers
· Processes 8 numbers simultaneously per register (vs 1 in std::sort)
· simd_small_sort: branchless sorting network for chunks ≤ 192 elements
· simd_merge_sort: splits array into 192-element chunks, sorts each, then merges repeatedly
· At n = 2,000,000: needs 14 merge passes to fully sort
Performance gaps we identified
· Gap 1 — Single-threaded: 11 cores sit idle
· Gap 2 — Merge hot-loop makes a branch decision 50M times/sort
· Gap 3 — No memory prefetching for large array merges
· Gap 4 — AVX-512 (wider registers) not used
· Gap 5 — Tile size hardcoded, ignores actual cache
Baseline already beats std::sort — our goal: push even further
n = 81
9.02× faster than std::sort
n = 2,187
4.34× faster than std::sort
n = 19,683
3.85× faster than std::sort
n = 531,441
2.84× faster than std::sort

## Slide 3
Project Scope & Approach
Five targeted improvements — each isolated and measured independently
In Scope
· Gap 1: OpenMP task-based multi-threading
· Gap 2: Branchless merge hot-loop
· Gap 3: Software memory prefetching
· Gap 4: AVX-512 simulation (tile doubling)
· Gap 5: Dynamic tile + pooled allocation
· Correctness check vs std::sort at every size
· Strong & weak scaling measurement
· Array sizes 10K → 2M floats
Out of Scope
· Real AVX-512 (hardware unavailable)
· Distributed / MPI parallelism
· GPU acceleration
· Non-x86 platforms
Tools
· Language: C++11
· Compiler: GCC 15 (-O3 -mavx2 -fopenmp)
· Threading: OpenMP 4.5 task model
· Timer: sokol_time.h (nanosecond precision)
· RNG: fixed seed 0xABCDEF01 (reproducible)
Methodology
· Each variant is a separate selectable option
· 100 timed runs per size — averaged
· Same random data for all variants (fair comparison)
· Correctness verified before any timing
· 5 correctness sizes × 7 variants = 35 tests
· Results from actual hardware runs — no simulation
· Scalability: thread sweep 1 → 12 threads

## Slide 4
Baseline — How simd_merge_sort Works
Two phases: branchless tile sort + recursive merge
Phase 1 — Tile Sort (simd_small_sort)
· Load up to 192 floats into 24 AVX2 registers (8 per register)
· Apply a fixed comparison network — like a tournament bracket
· All 8 comparisons happen in parallel — zero branches
· Output: a perfectly sorted 192-element chunk
Phase 2 — Bottom-up Merge (simd_merge_sort)
· Sorted chunks are merged in pairs: 192 → 384 → 768 → … → n
· At n = 2,000,000: requires 14 merge passes
· Merge hot-loop: pick smaller head element, load 8 floats, store
· This is where 65–75% of total runtime is spent → main target
Baseline speedup vs std::sort (actual measured values)
Array size
std::sort
SIMD baseline
Speedup
Fits in
Bottleneck
n = 81
0.19 ms
0.02 ms
9.0×
L1 cache
None — pure SIMD
n = 2,187
7.4 ms
1.7 ms
4.3×
L2 cache
Merge overhead
n = 531,441
3,303 ms
1,161 ms
2.8×
RAM
Memory bandwidth

## Slide 5
Five Optimizations — What We Changed and Why
Each targets a specific hardware bottleneck
Gap 1
OpenMP Multi-threading
12 cores instead of 1
Recursive task spawning parallelises both tile sort and merge tree phases. Depth = 4 → up to 16 concurrent tasks.
Gain: 2.7 – 3.0×
Gap 2
Branchless Merge
No mis-predicted branches
Replace if-branch in merge loop with arithmetic pointer selection. CPU calculates source address without guessing.
Gain: 1.0 – 1.1×
Gap 3
Memory Prefetch
Hide RAM latency
Issue prefetch hint 20 SIMD vectors (640 bytes) ahead. Covers ~80ns DRAM latency before the data is needed.
Gain: 1.0 – 1.2×
Gap 4
AVX-512 Simulation
One fewer merge pass
Create 384-element sorted runs (2× normal tile) then start merging from 384. Saves 1 of 14 merge passes at n = 2M.
Gain: 1.05 – 1.2×
Gap 5
Pooled Allocation
No malloc per merge call
Reuse a thread-local buffer instead of malloc/free for every merge. Eliminates thousands of allocations per sort.
Gain: 1.07 – 1.3×

## Slide 6
Results — Speedup Over Baseline at n = 500,000
Actual measured values · 100 runs averaged · Intel Core i7-12th Gen · 12 threads
Baseline
1.00×
Branchless
1.10×
Prefetch
1.16×
AVX-512 Sim
1.24×
DynTile
1.28×
OpenMP
2.66×
All Combined
3.04×
1.0×
Actual time (ms) at n=500K
1178 ms
1074 ms
1020 ms
948 ms
919 ms
443 ms
387 ms
All = OpenMP + Branchless + Prefetch + DynTile combined · Baseline = 1,178 ms (single-threaded, no optimizations)

## Slide 7
Speedup Across All Array Sizes
Actual benchmark output — 9 sizes from 10K to 2M elements
0.0×
0.7×
1.4×
2.1×
2.8×
3.5×
baseline
10K
50K
100K
250K
500K
750K
1M
1.5M
2M
Variant
All Combined
Best overall
OpenMP
Best at n>50K
DynTile
Best single-core
AVX-512 Sim
Saves 1 merge pass
Prefetch
Hides RAM latency
Branchless
No branch guessing

## Slide 8
Scalability — Strong Scaling & Thread Efficiency
Actual Option 8 output · n = 2,000,000 elements · thread sweep 1 → 12
Speedup vs threads (n=2M)
0.0×
1.0×
2.0×
3.0×
4.0×
1
2
3
4
6
8
10
12
Threads
Ideal (linear)
Actual
Actual measured values — n = 2,000,000
Threads
Time (ms)
Speedup
Efficiency
1
53.3
1.08×
108.0%
2
32.0
1.80×
89.8%
3
29.9
1.92×
64.2%
4
21.6
2.66×
66.6%
6
21.1
2.73×
45.5%
8
20.0
2.88×
36.0%
10
18.3
3.15×
31.5%
12
17.7
3.25×
27.1%
Phase breakdown (n = 2,000,000)
Tile-sort (parallel) 2.0%
Merge (serial) 98.0%
Merge = 98% serial → Amdahl ceiling ≈ 1.0× from parallelism alone
Why not 12× faster with 12 threads?
The merge step cannot be parallelised — it must run in order. This serial portion limits the maximum possible speedup (Amdahl's Law). We achieve 3.25× by parallelising everything else.

## Slide 9
Correctness & Full Comparison Table
Actual Option 7 output · 35/35 correctness tests passed · all 7 variants
Correctness verification — each variant sorted against std::sort reference
n = 10K 7 / 7 ✓
n = 100K 7 / 7 ✓
n = 500K 7 / 7 ✓
n = 1M 7 / 7 ✓
n = 2M 7 / 7 ✓
Performance table (ms) — 100 runs each · n from 10K to 2M
Size
Baseline
OpenMP
Branchless
Prefetch
DynTile
All
AVX512Sim
10K
11
26
12
12
10
26
11
50K
78
37
82
78
70
37
70
100K
171
68
170
185
157
65
154
250K
480
194
474
457
492
203
456
500K
1178
443
1074
1020
919
387
948
750K
1656
656
1707
1753
1458
611
1449
1M
2433
871
2359
2348
2026
861
2127
1.5M
3671
1363
3663
3618
3137
1333
3262
2M
5509
1890
5339
5278
4728
1895
4634
Green = best time for that row · Red = slower than baseline · Values in milliseconds

## Slide 10
Critical Analysis — What the Results Tell Us
Performance trends, bottlenecks, and deviations from expectation
OpenMP gives 2.7–3× — but not 12×
With 12 cores we expected closer to 12×. The merge step is 98% of runtime and cannot be parallelised — it must combine results in order. Amdahl's Law caps us at ~1.02× from parallelism alone at this phase split. OpenMP helps by parallelising the tile-sort phase and upper merge tree levels, giving us the observed 3×.
DynTile and AVX-512 Sim are the best single-core improvements
DynTile eliminates thousands of malloc/free calls (7–19% gain). AVX-512 Sim reduces merge passes from 14 to 13 at n=2M and also uses pooled memory (9–24% gain). Both outperform branchless and prefetch at all sizes — memory allocation overhead is a more significant bottleneck than branch misprediction.
Branchless merge: our first attempt was actually slower
The initial implementation loaded data from BOTH sides of the merge every iteration (2 loads vs 1). At large array sizes this doubled memory bandwidth usage — far more costly than the branch it replaced. We fixed it using arithmetic pointer selection (1 load per iteration, still branchless).
Prefetch helps less than expected at large sizes
The CPU's hardware prefetcher already detects the sequential access pattern and loads ahead automatically. Our software hints add only marginal benefit on top. The gain is visible at medium sizes (500K: 1.16×) but near-zero at 2M where the hardware prefetcher is fully warmed up.

## Slide 11
LLM Usage Disclosure & Reflection
07
⚠ PENDING
This section will cover: · Where and how LLMs were used during the project · Representative prompts and responses · Benefits observed and limitations encountered · Reflection on correctness, over-reliance risks, and academic integrity
To be completed before final submission

## Slide 12
Conclusions
09
3.25×
Peak speedup (12 threads, n=2M)
1.30×
Best single-core (DynTile, n=50K)
1.24×
AVX-512 Sim (n=500K)
35/35
Tests passed
Key Takeaways
Multi-threading is the dominant improvement.
OpenMP gives 3× at large sizes — parallelising both tile-sort and merge-tree phases across 12 threads. No single-core technique comes close.
Eliminating allocation overhead beats branch elimination.
Pooled memory (DynTile) and AVX-512 Sim outperform branchless and prefetch — malloc/free cost is a bigger bottleneck than branch misprediction on this hardware.
Measure everything — theory and practice diverge.
Our first branchless implementation was slower. Our prefetch added overhead via bounds checks. Both were fixed only because we measured the actual running time.
The serial merge step is the fundamental limit.
At n=2M the merge phase is 98% of runtime. Amdahl's Law caps parallel speedup at ~1.02×. Further gains require parallelising the merge itself — an open research problem.

## Slide 13
References
10
[1]
simd_bitonic
Open-source SIMD bitonic sort library. github.com/nlguillemot/simd_bitonic
[2]
Batcher (1968)
Sorting networks and their applications. AFIPS Spring Joint Computer Conference.
[3]
Intel SDM Vol. 2
Intel 64 and IA-32 Architectures Software Developer's Manual — AVX2 intrinsics.
[4]
OpenMP ARB
OpenMP Application Programming Interface, Version 4.5.
[5]
Amdahl (1967)
Validity of the single-processor approach. AFIPS Spring Joint Computer Conference.
[6]
Fog (2023)
Optimizing Software in C++ — Branch prediction, prefetch, cache hierarchy.
[7]
sokol_time.h
Cross-platform high-resolution timer. André Weissflog. MIT License.
All benchmarks reproducible: g++ -O3 -mavx2 -fopenmp -std=c++11 · fixed seed 0xABCDEF01